## Slide 1: STOCHASTIC MODELS - Advanced seminars - Rumor spreading over Networks
1
Notes: So today we gonna present the last module of this course that it is about queuieing networks….namely systems in which a number of queues are connected to each other by what it is called as... customer routing….
…where…for costumer routing we mean the path that costumers can follows among the queues of the network.
Just to give an idea on what we are going to talk…by refering to the network in the picture…. Here we have a multi-layer client-server architecture ….. requests come from outside…and are taken in charge and elaborated by the first set of queues…than if the request is accomplished that job leaves the system following one of the possible leaving-path.
Otherwise…If that request requires other operations…related messages are delivered to the layer 1 and if necessary from layer 1 to layer 2….
Let us further note that sometimes it may also occur that an operation need a cross check…. and thus the costumer routing can also consider the presence of loops like this….or this…
In general we have that when a customer is serviced at one node…then… it can join another node and queue for service, or simply leave the system.
Ah…notice that in this contest… we will often refer to the queues that constitute the network as nodes…

## Slide 2: Rumor spreading over Networks
Rumor is an important form of social communication, and the spread of rumors plays a significant role in a variety of human affairs
In this module, we shall look at some highly simpliﬁed models of information spread, with the goal of addressing precise questions: “How fast is the rumor spreading?”
How do technologies diﬀuse within or across societies?
Those are some example motivating the study of information spread in networks
How people are influenced by trends, and fashions take hold?
How do people learn about news/job opportunities or else?
Other examples comes from synthetic networks like the social networks, or P2P WSN, and multi-agents networks, where it may be important to disseminate information rapidly
It allows to find an answer to the questions, like:
Notes: Here just to remark the importance of queuing networks in telecommunication systems we have another example…for instance…the Internet… that….as you know…. It works by means of a complex architecture where packets flows are processed by many routers, each modeled by a queue.
In particular we have that packets enter in the network because generated from different sources…. and with different destinations…
Then…. they arrive to nodes in a stochastic fashion…and then…each router asynchronously elaborates them…
Of course notice that.. if the traffic intensity exceed some given quantities …well some traffic is lost due to buffer overflows…
Let us further note that queuing networks are successfully used not only to solve resource allocation problems in telecommunication but…. Of course….whenever a flow of jobs need to be processed, independently by the fact that their arrivals and services are either synchronous or asynchronous, or either stochastic or deterministic.
In particular we have that all the results we are going to see are useful to determines in an easy way the system performance…and also to evaluate…. for resource allocation purposes…. the resources need such that a complex client-server architecture works while satisfying some QoS specifications.
Specification that could be expressed in term of time spent in the system…or in term of the buffer capacity … and that of course depends on the allocated resources…that means the number of servers per queue, their service rate… the buffer capacity … furthermore it is easy understand that all those quantities are further influenced by the costumer routing that express…in terms or probability….all the possible paths that a costumer can follows within the network.

## Slide 3: Asynchronous Rumor spreading over networks
This is called the “push model” as information is “pushed” form to
Consider a communication network withnodes
Assume: The communication graph is complete (for the moment)
Assume: Among the nodes, only nodes initially knows the “rumor”
if knows the rumor and doesn’t, then informs , otherwise there is no change
Assume: Each node has a local clock “ticking” as a Poisson process with rate
Then: When there is a jump on node becomes active
Question: Starting at and let be the ﬁrst time all the nodes know the rumor.
What about , and how it depends by graph’s size “”?
This implies each node has neighbors to which communicate
Definition: A graph is complete if there is an edge between every pair of nodes.
Definition The neighbor set of node
it pick-up a node , randomly and uniformly over and communicate with it
Notes: Here just to remark the importance of queuing networks in telecommunication systems we have another example…for instance…the Internet… that….as you know…. It works by means of a complex architecture where packets flows are processed by many routers, each modeled by a queue.
In particular we have that packets enter in the network because generated from different sources…. and with different destinations…
Then…. they arrive to nodes in a stochastic fashion…and then…each router asynchronously elaborates them…
Of course notice that.. if the traffic intensity exceed some given quantities …well some traffic is lost due to buffer overflows…
Let us further note that queuing networks are successfully used not only to solve resource allocation problems in telecommunication but…. Of course….whenever a flow of jobs need to be processed, independently by the fact that their arrivals and services are either synchronous or asynchronous, or either stochastic or deterministic.
In particular we have that all the results we are going to see are useful to determines in an easy way the system performance…and also to evaluate…. for resource allocation purposes…. the resources need such that a complex client-server architecture works while satisfying some QoS specifications.
Specification that could be expressed in term of time spent in the system…or in term of the buffer capacity … and that of course depends on the allocated resources…that means the number of servers per queue, their service rate… the buffer capacity … furthermore it is easy understand that all those quantities are further influenced by the costumer routing that express…in terms or probability….all the possible paths that a costumer can follows within the network.

## Slide 4: Rumor spreading over complete graphs: CT-MC model
Having local clocks, corresponds to single clock ticking at a rate (superposition of Poisson processes), where
Note: From the point of view of a node knowing the rumor, the fact it wake-ups with a rate does not implies the spreading rate will be the same (e.g. it may pick an already informed node…)
  Event a: among the many nodes, one of the knowing the rumor is waked-up,
  Event b: among the available arcs, is picked-up a not informed node
Indeed, since the random splitting of a Poisson Process is Poisson as well, the mean time to inform a new node is the time to the first jump of a splitting on at a rate, scaled by the Joint probability of the joint events «a,b»
  Let be the process counting the #nodes knowing the rumour, then the rumor spreading can be modelled as a non-uniform CT-BDP with birth-rate
  Since is the only absorbing state, sooner or later, all nodes will be informed with probability 1.
Notes: Here just to remark the importance of queuing networks in telecommunication systems we have another example…for instance…the Internet… that….as you know…. It works by means of a complex architecture where packets flows are processed by many routers, each modeled by a queue.
In particular we have that packets enter in the network because generated from different sources…. and with different destinations…
Then…. they arrive to nodes in a stochastic fashion…and then…each router asynchronously elaborates them…
Of course notice that.. if the traffic intensity exceed some given quantities …well some traffic is lost due to buffer overflows…
Let us further note that queuing networks are successfully used not only to solve resource allocation problems in telecommunication but…. Of course….whenever a flow of jobs need to be processed, independently by the fact that their arrivals and services are either synchronous or asynchronous, or either stochastic or deterministic.
In particular we have that all the results we are going to see are useful to determines in an easy way the system performance…and also to evaluate…. for resource allocation purposes…. the resources need such that a complex client-server architecture works while satisfying some QoS specifications.
Specification that could be expressed in term of time spent in the system…or in term of the buffer capacity … and that of course depends on the allocated resources…that means the number of servers per queue, their service rate… the buffer capacity … furthermore it is easy understand that all those quantities are further influenced by the costumer routing that express…in terms or probability….all the possible paths that a costumer can follows within the network.

## Slide 5: Analysis as a function of the network size “”
Recalling , where is the mean time to absorption, one conclude:
Due to independence, and because (harmonic series), (Basel problem)
From that, and by means of the Chebishev’s inequality one can further conclude
Interpretation: The fluctuaion around the mean time is bounded, indepedent by , and for a given decrease with . Namely will not be much different than .
Notes: Here just to remark the importance of queuing networks in telecommunication systems we have another example…for instance…the Internet… that….as you know…. It works by means of a complex architecture where packets flows are processed by many routers, each modeled by a queue.
In particular we have that packets enter in the network because generated from different sources…. and with different destinations…
Then…. they arrive to nodes in a stochastic fashion…and then…each router asynchronously elaborates them…
Of course notice that.. if the traffic intensity exceed some given quantities …well some traffic is lost due to buffer overflows…
Let us further note that queuing networks are successfully used not only to solve resource allocation problems in telecommunication but…. Of course….whenever a flow of jobs need to be processed, independently by the fact that their arrivals and services are either synchronous or asynchronous, or either stochastic or deterministic.
In particular we have that all the results we are going to see are useful to determines in an easy way the system performance…and also to evaluate…. for resource allocation purposes…. the resources need such that a complex client-server architecture works while satisfying some QoS specifications.
Specification that could be expressed in term of time spent in the system…or in term of the buffer capacity … and that of course depends on the allocated resources…that means the number of servers per queue, their service rate… the buffer capacity … furthermore it is easy understand that all those quantities are further influenced by the costumer routing that express…in terms or probability….all the possible paths that a costumer can follows within the network.

## Slide 6: Order of Complexities
Thus, as increases, the rumour spreading time-complexity grows as
Below some notion on time-complexities are explained:
Constant: The algorithm runs for the same amount of time every time irrespective of the problem size,
Linear: The algorithm runtime is linearly proportional to the problem size,
Exponential: The algorithm runtime depends on a power of the input-size, this one of the most horrible use-cases , (see NP-hard problems)
Logarithmic: The algorithm runtime increases very slowly compared to an increase in input size i.e. logarithm of input size, (thus seconds)
Polinomial: The algorithm runtime depends on the input value raised to an exponent. It is one of the worst use-cases, indeed: (see P- and NP-problems)
This fact numerically justify the reason why gossips are spread very fast in a social networks
Notes: Here just to remark the importance of queuing networks in telecommunication systems we have another example…for instance…the Internet… that….as you know…. It works by means of a complex architecture where packets flows are processed by many routers, each modeled by a queue.
In particular we have that packets enter in the network because generated from different sources…. and with different destinations…
Then…. they arrive to nodes in a stochastic fashion…and then…each router asynchronously elaborates them…
Of course notice that.. if the traffic intensity exceed some given quantities …well some traffic is lost due to buffer overflows…
Let us further note that queuing networks are successfully used not only to solve resource allocation problems in telecommunication but…. Of course….whenever a flow of jobs need to be processed, independently by the fact that their arrivals and services are either synchronous or asynchronous, or either stochastic or deterministic.
In particular we have that all the results we are going to see are useful to determines in an easy way the system performance…and also to evaluate…. for resource allocation purposes…. the resources need such that a complex client-server architecture works while satisfying some QoS specifications.
Specification that could be expressed in term of time spent in the system…or in term of the buffer capacity … and that of course depends on the allocated resources…that means the number of servers per queue, their service rate… the buffer capacity … furthermore it is easy understand that all those quantities are further influenced by the costumer routing that express…in terms or probability….all the possible paths that a costumer can follows within the network.

## Slide 7: Rumor spreading over generic Graphs
Let us now study how the communication topology affects the time
Assume: Graph is arbitrary and strongly connected ( an oriented path ), and let be the probability talks with , where
  As for the previous case, let be the SP counting the #nodes knowing the rumor, with . Even now, the rumor dissemination can be modelled as a CT-MC
  Definition: The conductance of a nonegative matrix is
  Example:
  Since is now arbitrary (), the probability a new node is informed depends by all the random sets can be reached at time and their neighbor set. Thus, since , yields
  It is easy understand the analysis is impracticable when is large.
  Interpretation: It gives a measure of the worst-case
where
  information dissemination flow between different parts of a graph.
  To draw upperbound conclusions for , the “matrix conductance” concept is helpful
Notes: Here just to remark the importance of queuing networks in telecommunication systems we have another example…for instance…the Internet… that….as you know…. It works by means of a complex architecture where packets flows are processed by many routers, each modeled by a queue.
In particular we have that packets enter in the network because generated from different sources…. and with different destinations…
Then…. they arrive to nodes in a stochastic fashion…and then…each router asynchronously elaborates them…
Of course notice that.. if the traffic intensity exceed some given quantities …well some traffic is lost due to buffer overflows…
Let us further note that queuing networks are successfully used not only to solve resource allocation problems in telecommunication but…. Of course….whenever a flow of jobs need to be processed, independently by the fact that their arrivals and services are either synchronous or asynchronous, or either stochastic or deterministic.
In particular we have that all the results we are going to see are useful to determines in an easy way the system performance…and also to evaluate…. for resource allocation purposes…. the resources need such that a complex client-server architecture works while satisfying some QoS specifications.
Specification that could be expressed in term of time spent in the system…or in term of the buffer capacity … and that of course depends on the allocated resources…that means the number of servers per queue, their service rate… the buffer capacity … furthermore it is easy understand that all those quantities are further influenced by the costumer routing that express…in terms or probability….all the possible paths that a costumer can follows within the network.

## Slide 8: Rumor spreading over general graphs (cont’d)
However, from that, we can upper-estimate by means of the conductance matrix
  Thus, from that, an upper-bound for is obtained
  Morevoer, by the Markov inequality, we can also see
  which tends to zero as . Thus, the r.v. is of order in probability.
  Example: If is complete, as in the previous case, then it results
  Thus:
Notes: Here just to remark the importance of queuing networks in telecommunication systems we have another example…for instance…the Internet… that….as you know…. It works by means of a complex architecture where packets flows are processed by many routers, each modeled by a queue.
In particular we have that packets enter in the network because generated from different sources…. and with different destinations…
Then…. they arrive to nodes in a stochastic fashion…and then…each router asynchronously elaborates them…
Of course notice that.. if the traffic intensity exceed some given quantities …well some traffic is lost due to buffer overflows…
Let us further note that queuing networks are successfully used not only to solve resource allocation problems in telecommunication but…. Of course….whenever a flow of jobs need to be processed, independently by the fact that their arrivals and services are either synchronous or asynchronous, or either stochastic or deterministic.
In particular we have that all the results we are going to see are useful to determines in an easy way the system performance…and also to evaluate…. for resource allocation purposes…. the resources need such that a complex client-server architecture works while satisfying some QoS specifications.
Specification that could be expressed in term of time spent in the system…or in term of the buffer capacity … and that of course depends on the allocated resources…that means the number of servers per queue, their service rate… the buffer capacity … furthermore it is easy understand that all those quantities are further influenced by the costumer routing that express…in terms or probability….all the possible paths that a costumer can follows within the network.

## Slide 9: Simulation
clc, clear all, close all, rng(6)
% Initialize the simulation
N = 10; % number of nodes
S = zeros(1, N); % state of each node (0 = unaware, 1 = aware)
S(1) = 1; % node 1 knows the rumor
t = 0; % interaction time
% Create the complete graph matrix
G = ones(N) - eye(N);
% Agents collect the agents’ status at each iteration until
Agents=[S];
while sum(S)< N % while there are still unaware nodes
  % Enstablish a random comm. between 2 nodes (the 1st knows the rumor)
  node_indices = randperm(N, 2)
  % Push model
  if S(node_indices(1))==1
  S(node_indices(2)) = S(node_indices(1));
  end
  % Update the interaction time in accordance with an Exp(1/N), rate 10
  t = [t;t(end) + exprnd(1/N)];
  Agents=[Agents;S];
end
Notes: Here just to remark the importance of queuing networks in telecommunication systems we have another example…for instance…the Internet… that….as you know…. It works by means of a complex architecture where packets flows are processed by many routers, each modeled by a queue.
In particular we have that packets enter in the network because generated from different sources…. and with different destinations…
Then…. they arrive to nodes in a stochastic fashion…and then…each router asynchronously elaborates them…
Of course notice that.. if the traffic intensity exceed some given quantities …well some traffic is lost due to buffer overflows…
Let us further note that queuing networks are successfully used not only to solve resource allocation problems in telecommunication but…. Of course….whenever a flow of jobs need to be processed, independently by the fact that their arrivals and services are either synchronous or asynchronous, or either stochastic or deterministic.
In particular we have that all the results we are going to see are useful to determines in an easy way the system performance…and also to evaluate…. for resource allocation purposes…. the resources need such that a complex client-server architecture works while satisfying some QoS specifications.
Specification that could be expressed in term of time spent in the system…or in term of the buffer capacity … and that of course depends on the allocated resources…that means the number of servers per queue, their service rate… the buffer capacity … furthermore it is easy understand that all those quantities are further influenced by the costumer routing that express…in terms or probability….all the possible paths that a costumer can follows within the network.

## Slide 10: Simulation
% Plot the agents states
figure(1)
  for i=2:10
  subplot(9,1,i-1)
  stairs(t, Agents(:,i), '-o');
  ylabel(['Ag. ' num2str(i)]);
  ylim([0,2])
  grid
  end
  xlabel(‘time');
Notes: Here just to remark the importance of queuing networks in telecommunication systems we have another example…for instance…the Internet… that….as you know…. It works by means of a complex architecture where packets flows are processed by many routers, each modeled by a queue.
In particular we have that packets enter in the network because generated from different sources…. and with different destinations…
Then…. they arrive to nodes in a stochastic fashion…and then…each router asynchronously elaborates them…
Of course notice that.. if the traffic intensity exceed some given quantities …well some traffic is lost due to buffer overflows…
Let us further note that queuing networks are successfully used not only to solve resource allocation problems in telecommunication but…. Of course….whenever a flow of jobs need to be processed, independently by the fact that their arrivals and services are either synchronous or asynchronous, or either stochastic or deterministic.
In particular we have that all the results we are going to see are useful to determines in an easy way the system performance…and also to evaluate…. for resource allocation purposes…. the resources need such that a complex client-server architecture works while satisfying some QoS specifications.
Specification that could be expressed in term of time spent in the system…or in term of the buffer capacity … and that of course depends on the allocated resources…that means the number of servers per queue, their service rate… the buffer capacity … furthermore it is easy understand that all those quantities are further influenced by the costumer routing that express…in terms or probability….all the possible paths that a costumer can follows within the network.