## Slide 1: STOCHASTIC MODELS - Convex optimization over Distributed Networks
1
Notes: So today we gonna present the last module of this course that it is about queuieing networks….namely systems in which a number of queues are connected to each other by what it is called as... customer routing….
…where…for costumer routing we mean the path that costumers can follows among the queues of the network.
Just to give an idea on what we are going to talk…by refering to the network in the picture…. Here we have a multi-layer client-server architecture ….. requests come from outside…and are taken in charge and elaborated by the first set of queues…than if the request is accomplished that job leaves the system following one of the possible leaving-path.
Otherwise…If that request requires other operations…related messages are delivered to the layer 1 and if necessary from layer 1 to layer 2….
Let us further note that sometimes it may also occur that an operation need a cross check…. and thus the costumer routing can also consider the presence of loops like this….or this…
In general we have that when a customer is serviced at one node…then… it can join another node and queue for service, or simply leave the system.
Ah…notice that in this contest… we will often refer to the queues that constitute the network as nodes…

## Slide 2: Motivating considerations
This is mainly motivated by the explosion in size and complexity of data sets used in statistical machine learning, where optimization is used for parameter training, and for applications in Large-Scale Systems decision making problems
In recent years, there has been a renewed research interest towards ﬁnding efﬁcient algorithms for solving convex optimization problems in parallel or distributed fashion
In the following basic notions on centralized and distributed convex optimization algorithms are discussed by exploiting results on System Theory analysis
Convex optimization has practical applications for the following:
Machine learning (multi-class classifiers & unsupervised learning)
and all those applications implemented over a network and/or on a IoT-based control infrastructure where nodes with limited capabilities have to perform decision-making tasks beyond their “local” environment knowledge
Load balancing optimization
Distributed localization using wireless signals
Distributed coordination of multi-robot platoon
Network Utility Maximization problems
Electricity generation optimization
Notes: Here just to remark the importance of queuing networks in telecommunication systems we have another example…for instance…the Internet… that….as you know…. It works by means of a complex architecture where packets flows are processed by many routers, each modeled by a queue.
In particular we have that packets enter in the network because generated from different sources…. and with different destinations…
Then…. they arrive to nodes in a stochastic fashion…and then…each router asynchronously elaborates them…
Of course notice that.. if the traffic intensity exceed some given quantities …well some traffic is lost due to buffer overflows…
Let us further note that queuing networks are successfully used not only to solve resource allocation problems in telecommunication but…. Of course….whenever a flow of jobs need to be processed, independently by the fact that their arrivals and services are either synchronous or asynchronous, or either stochastic or deterministic.
In particular we have that all the results we are going to see are useful to determines in an easy way the system performance…and also to evaluate…. for resource allocation purposes…. the resources need such that a complex client-server architecture works while satisfying some QoS specifications.
Specification that could be expressed in term of time spent in the system…or in term of the buffer capacity … and that of course depends on the allocated resources…that means the number of servers per queue, their service rate… the buffer capacity … furthermore it is easy understand that all those quantities are further influenced by the costumer routing that express…in terms or probability….all the possible paths that a costumer can follows within the network.

## Slide 3: Some notion on convexity
A scalar function is called convex if
If the inequality holds strictly is called strictly convex, thus it has unique minimun
Example 1: (unique min.)
Lemma 1: If is differentiable (), convexity is equivalent to
Theorem (Fermat): Let differentiable, and be a local minimum of . Then
Proof: Let and suppose , with
this contradict the minimun definition, thus
Example 1 (cont’d):
Notes: Here just to remark the importance of queuing networks in telecommunication systems we have another example…for instance…the Internet… that….as you know…. It works by means of a complex architecture where packets flows are processed by many routers, each modeled by a queue.
In particular we have that packets enter in the network because generated from different sources…. and with different destinations…
Then…. they arrive to nodes in a stochastic fashion…and then…each router asynchronously elaborates them…
Of course notice that.. if the traffic intensity exceed some given quantities …well some traffic is lost due to buffer overflows…
Let us further note that queuing networks are successfully used not only to solve resource allocation problems in telecommunication but…. Of course….whenever a flow of jobs need to be processed, independently by the fact that their arrivals and services are either synchronous or asynchronous, or either stochastic or deterministic.
In particular we have that all the results we are going to see are useful to determines in an easy way the system performance…and also to evaluate…. for resource allocation purposes…. the resources need such that a complex client-server architecture works while satisfying some QoS specifications.
Specification that could be expressed in term of time spent in the system…or in term of the buffer capacity … and that of course depends on the allocated resources…that means the number of servers per queue, their service rate… the buffer capacity … furthermore it is easy understand that all those quantities are further influenced by the costumer routing that express…in terms or probability….all the possible paths that a costumer can follows within the network.

## Slide 4: Unconstrained convex optimization: The Gradient Method
Theorem: Let be a convex function, bounded from below, with the gradient satisfying
Let then , and monotonically decrease to
Let be convex, differentiable and bounded from below , to solve
the simplest way, since , is by minimizing its gradient, which, due to convexity, is an increasing function (). Thus, one may construct the iteration sequence as
Proof: By the fundamental theorem of calculus , specified along the path “” where are 2 decision vectors values, it yields:
Then, letting and , it yields
Notes: Here just to remark the importance of queuing networks in telecommunication systems we have another example…for instance…the Internet… that….as you know…. It works by means of a complex architecture where packets flows are processed by many routers, each modeled by a queue.
In particular we have that packets enter in the network because generated from different sources…. and with different destinations…
Then…. they arrive to nodes in a stochastic fashion…and then…each router asynchronously elaborates them…
Of course notice that.. if the traffic intensity exceed some given quantities …well some traffic is lost due to buffer overflows…
Let us further note that queuing networks are successfully used not only to solve resource allocation problems in telecommunication but…. Of course….whenever a flow of jobs need to be processed, independently by the fact that their arrivals and services are either synchronous or asynchronous, or either stochastic or deterministic.
In particular we have that all the results we are going to see are useful to determines in an easy way the system performance…and also to evaluate…. for resource allocation purposes…. the resources need such that a complex client-server architecture works while satisfying some QoS specifications.
Specification that could be expressed in term of time spent in the system…or in term of the buffer capacity … and that of course depends on the allocated resources…that means the number of servers per queue, their service rate… the buffer capacity … furthermore it is easy understand that all those quantities are further influenced by the costumer routing that express…in terms or probability….all the possible paths that a costumer can follows within the network.

## Slide 5: Unconstrained convex optimization: The Gradient descent Method
Then, by exploting (3), i.e. , it yields
By summing the inequalities from to over , we obtain
From which, it is easy note
Thus, the series is summable:
Example 1 (con’t): Consider .
Further .
Remark: Let , the convergence can be speed-up as , where now
Corollary: If , a CT gradient descent is implemented. Moreover, if is strictly convex, correspond to the unique stable equilibrium of .
Notes: Here just to remark the importance of queuing networks in telecommunication systems we have another example…for instance…the Internet… that….as you know…. It works by means of a complex architecture where packets flows are processed by many routers, each modeled by a queue.
In particular we have that packets enter in the network because generated from different sources…. and with different destinations…
Then…. they arrive to nodes in a stochastic fashion…and then…each router asynchronously elaborates them…
Of course notice that.. if the traffic intensity exceed some given quantities …well some traffic is lost due to buffer overflows…
Let us further note that queuing networks are successfully used not only to solve resource allocation problems in telecommunication but…. Of course….whenever a flow of jobs need to be processed, independently by the fact that their arrivals and services are either synchronous or asynchronous, or either stochastic or deterministic.
In particular we have that all the results we are going to see are useful to determines in an easy way the system performance…and also to evaluate…. for resource allocation purposes…. the resources need such that a complex client-server architecture works while satisfying some QoS specifications.
Specification that could be expressed in term of time spent in the system…or in term of the buffer capacity … and that of course depends on the allocated resources…that means the number of servers per queue, their service rate… the buffer capacity … furthermore it is easy understand that all those quantities are further influenced by the costumer routing that express…in terms or probability….all the possible paths that a costumer can follows within the network.

## Slide 6: Convex optimization with equality constraints
Consider the following constrained optimization problem.
To provide the main idea and simplifying derivations, we assume: a) (full row-rank); b) differentiable and strictly-convex; c) optimization is made in continuous-time
Lagrange Multiplier theory allows to convert (4) into the “Unconstrained Lagrangian Dual Problem”
where , is called Lagrange multiplier, and introduces a penalty positive term on the objective function such that
If is mets , thus can be reached following
Note: Lagrange Multipliers Theory cause the critical point to occur at a saddle point. Indeed, results convex w.r.t. to and concave w.r.t. .
If not, since is maximized, small deviations on leads to increase a lot. This implies (5) give more priority to the constrain satisfaction rather than .
Notes: Here just to remark the importance of queuing networks in telecommunication systems we have another example…for instance…the Internet… that….as you know…. It works by means of a complex architecture where packets flows are processed by many routers, each modeled by a queue.
In particular we have that packets enter in the network because generated from different sources…. and with different destinations…
Then…. they arrive to nodes in a stochastic fashion…and then…each router asynchronously elaborates them…
Of course notice that.. if the traffic intensity exceed some given quantities …well some traffic is lost due to buffer overflows…
Let us further note that queuing networks are successfully used not only to solve resource allocation problems in telecommunication but…. Of course….whenever a flow of jobs need to be processed, independently by the fact that their arrivals and services are either synchronous or asynchronous, or either stochastic or deterministic.
In particular we have that all the results we are going to see are useful to determines in an easy way the system performance…and also to evaluate…. for resource allocation purposes…. the resources need such that a complex client-server architecture works while satisfying some QoS specifications.
Specification that could be expressed in term of time spent in the system…or in term of the buffer capacity … and that of course depends on the allocated resources…that means the number of servers per queue, their service rate… the buffer capacity … furthermore it is easy understand that all those quantities are further influenced by the costumer routing that express…in terms or probability….all the possible paths that a costumer can follows within the network.

## Slide 7: Convex optimization with equality constraints
To solve the problem
A CT solver may follow w.r.t. and w.r.t. , as:
Theorem: Consider (6), for any initial values and , we have
To study the solver’s convergence, it is convenient study the dynamic of , namely
Proof: Let be a stazionary point of (6), it satisfies and . Moreover, under the current assumptions such equilibrium is unique, and corresponds to the solution of (5).
Lyap. Theorem: Let be an equilibrium of . If and (pos. def. ) such that (neg. semi-def. ), is stable. If (neg. def. ), is asympt. stable
LaSalle’s Invariance Principle: Let (i.e. also for some ). If the Invariant Set satisyfing contains no other trajectories except , then is asympt. stable.
Equilibrum stability of nonlin. dyn. systems is studied through the Lyapunov direct method
Notes: Here just to remark the importance of queuing networks in telecommunication systems we have another example…for instance…the Internet… that….as you know…. It works by means of a complex architecture where packets flows are processed by many routers, each modeled by a queue.
In particular we have that packets enter in the network because generated from different sources…. and with different destinations…
Then…. they arrive to nodes in a stochastic fashion…and then…each router asynchronously elaborates them…
Of course notice that.. if the traffic intensity exceed some given quantities …well some traffic is lost due to buffer overflows…
Let us further note that queuing networks are successfully used not only to solve resource allocation problems in telecommunication but…. Of course….whenever a flow of jobs need to be processed, independently by the fact that their arrivals and services are either synchronous or asynchronous, or either stochastic or deterministic.
In particular we have that all the results we are going to see are useful to determines in an easy way the system performance…and also to evaluate…. for resource allocation purposes…. the resources need such that a complex client-server architecture works while satisfying some QoS specifications.
Specification that could be expressed in term of time spent in the system…or in term of the buffer capacity … and that of course depends on the allocated resources…that means the number of servers per queue, their service rate… the buffer capacity … furthermore it is easy understand that all those quantities are further influenced by the costumer routing that express…in terms or probability….all the possible paths that a costumer can follows within the network.

## Slide 8: Physical-based stability understanding example
Example: Consider a pendolum with friction
To further conclude if is asymptotically stable we need now study (8) initialized on
Equilibrium points are the solutions of , if we assume
To study , ‘energetic’ or ‘arbitrarily chosen’ positive def. functions (e.g. norms) of can be used:
Note: Thus is simply stable, and the invariant set solution of will be reached.
Note: Since implies both and then . Moreover, since only satisfies the invariance of , then . Thus, is asymp. stable.
Let , by simple manipulations
Notes: Here just to remark the importance of queuing networks in telecommunication systems we have another example…for instance…the Internet… that….as you know…. It works by means of a complex architecture where packets flows are processed by many routers, each modeled by a queue.
In particular we have that packets enter in the network because generated from different sources…. and with different destinations…
Then…. they arrive to nodes in a stochastic fashion…and then…each router asynchronously elaborates them…
Of course notice that.. if the traffic intensity exceed some given quantities …well some traffic is lost due to buffer overflows…
Let us further note that queuing networks are successfully used not only to solve resource allocation problems in telecommunication but…. Of course….whenever a flow of jobs need to be processed, independently by the fact that their arrivals and services are either synchronous or asynchronous, or either stochastic or deterministic.
In particular we have that all the results we are going to see are useful to determines in an easy way the system performance…and also to evaluate…. for resource allocation purposes…. the resources need such that a complex client-server architecture works while satisfying some QoS specifications.
Specification that could be expressed in term of time spent in the system…or in term of the buffer capacity … and that of course depends on the allocated resources…that means the number of servers per queue, their service rate… the buffer capacity … furthermore it is easy understand that all those quantities are further influenced by the costumer routing that express…in terms or probability….all the possible paths that a costumer can follows within the network.

## Slide 9: Constrained convex optimization with equality constraints
Consider, e.g., as a candidate Lyap. Func. the norm distance to
By differentiating it, and thanks to Lemma 1:
To say more, let’s study what happen after the Invariant Set is reached
By intializing (11) on , it yields:
Since implies and , this further implies Thus, since the only constant satisfying is . It results is asym. stable and thus will be reached
Note: Such equilibrium is also global. Indeed, since is strictly convex, it results has a unique equilibrium point.
Remark: If is NOT CONVEX has many equilibrium points,
some locally stable (minimum), some unstable (maximum).
If so, will converge to the closest minimum to .
To find the optimum heuristics are needed (e.g. execute algorithm for many )
Note: By discretizing (6) the results can be extended to the DT setting, for small enough .
is stable, however since is function of
only, while noting can be stated for
Notes: Here just to remark the importance of queuing networks in telecommunication systems we have another example…for instance…the Internet… that….as you know…. It works by means of a complex architecture where packets flows are processed by many routers, each modeled by a queue.
In particular we have that packets enter in the network because generated from different sources…. and with different destinations…
Then…. they arrive to nodes in a stochastic fashion…and then…each router asynchronously elaborates them…
Of course notice that.. if the traffic intensity exceed some given quantities …well some traffic is lost due to buffer overflows…
Let us further note that queuing networks are successfully used not only to solve resource allocation problems in telecommunication but…. Of course….whenever a flow of jobs need to be processed, independently by the fact that their arrivals and services are either synchronous or asynchronous, or either stochastic or deterministic.
In particular we have that all the results we are going to see are useful to determines in an easy way the system performance…and also to evaluate…. for resource allocation purposes…. the resources need such that a complex client-server architecture works while satisfying some QoS specifications.
Specification that could be expressed in term of time spent in the system…or in term of the buffer capacity … and that of course depends on the allocated resources…that means the number of servers per queue, their service rate… the buffer capacity … furthermore it is easy understand that all those quantities are further influenced by the costumer routing that express…in terms or probability….all the possible paths that a costumer can follows within the network.

## Slide 10: Convex optimization with inequality constraints
Consider the following constrained optimization problem.
Requirement: These constraints, even not linear (e.g. ), must satisfy the Slater's condition i.e. ( must be interior to the domain identified by the intersection constraints).
From (12), let large enough, then the solution of (12) can be approximated by:
Note: Because then is intrinsecally verified, and (13) plays as an optimization with equality constraints it can solved as the unconstrained Lagrangian dual problem, where:
Note: Inequalities in (12) are replaced by a barrier cost function depending by the slack variables aimed at penalizing the optimization, e.g., as then .
Let , , then where larger is closer is to
as
and is the Lagrangian function
Notes: Here just to remark the importance of queuing networks in telecommunication systems we have another example…for instance…the Internet… that….as you know…. It works by means of a complex architecture where packets flows are processed by many routers, each modeled by a queue.
In particular we have that packets enter in the network because generated from different sources…. and with different destinations…
Then…. they arrive to nodes in a stochastic fashion…and then…each router asynchronously elaborates them…
Of course notice that.. if the traffic intensity exceed some given quantities …well some traffic is lost due to buffer overflows…
Let us further note that queuing networks are successfully used not only to solve resource allocation problems in telecommunication but…. Of course….whenever a flow of jobs need to be processed, independently by the fact that their arrivals and services are either synchronous or asynchronous, or either stochastic or deterministic.
In particular we have that all the results we are going to see are useful to determines in an easy way the system performance…and also to evaluate…. for resource allocation purposes…. the resources need such that a complex client-server architecture works while satisfying some QoS specifications.
Specification that could be expressed in term of time spent in the system…or in term of the buffer capacity … and that of course depends on the allocated resources…that means the number of servers per queue, their service rate… the buffer capacity … furthermore it is easy understand that all those quantities are further influenced by the costumer routing that express…in terms or probability….all the possible paths that a costumer can follows within the network.

## Slide 11: Distributed convex optimization
Consider an undirected network of agents aimed at solving the decision making problem
where is a common objective function, and are private and strictly convex functions
Remark: Since agent knows only they need to collaborate over to solve (13), i.e. they need to find a consensus over on a common value such that
Note: Assume undirected is not restrictive, especially, if gossip interactions are implemented.
Examples: a) can be viewed as the optimal power, a set of controllable loads are planned to absorbe to avoid peaks; b) or the optimal power a set generator should inject to meet some demand.
Thus, solve the unconstrained problem (13) in a distributed way, and under the communication constraints over , is equivalent to solve the next problem with the equality constraints:
Note: If depends only by as in (13), we say (13) is separable (i.e. solve (13) is equivalent to solve separately , ). IF NOT, suboptimal heuristics needs to be devised.
Thus, (14) can be solved by the Lagrange multipl. methods, where must satisfy
Notes: Here just to remark the importance of queuing networks in telecommunication systems we have another example…for instance…the Internet… that….as you know…. It works by means of a complex architecture where packets flows are processed by many routers, each modeled by a queue.
In particular we have that packets enter in the network because generated from different sources…. and with different destinations…
Then…. they arrive to nodes in a stochastic fashion…and then…each router asynchronously elaborates them…
Of course notice that.. if the traffic intensity exceed some given quantities …well some traffic is lost due to buffer overflows…
Let us further note that queuing networks are successfully used not only to solve resource allocation problems in telecommunication but…. Of course….whenever a flow of jobs need to be processed, independently by the fact that their arrivals and services are either synchronous or asynchronous, or either stochastic or deterministic.
In particular we have that all the results we are going to see are useful to determines in an easy way the system performance…and also to evaluate…. for resource allocation purposes…. the resources need such that a complex client-server architecture works while satisfying some QoS specifications.
Specification that could be expressed in term of time spent in the system…or in term of the buffer capacity … and that of course depends on the allocated resources…that means the number of servers per queue, their service rate… the buffer capacity … furthermore it is easy understand that all those quantities are further influenced by the costumer routing that express…in terms or probability….all the possible paths that a costumer can follows within the network.

## Slide 12: Distributed CT convex optimization
Thus, (14) can be solved by:
From which the next dynamical solver can be derived
Note: Since the original problem is separable, (16) can easily be implemented in a distributed fashion over the multi-agents system framework.
Let be the neighbours set of agent , the next agent control solves (16):
Thus, let the agent dynamic be as:
Note: The block diagram shows can be viewed as an integral control which argument is the consensus term
Notes: Here just to remark the importance of queuing networks in telecommunication systems we have another example…for instance…the Internet… that….as you know…. It works by means of a complex architecture where packets flows are processed by many routers, each modeled by a queue.
In particular we have that packets enter in the network because generated from different sources…. and with different destinations…
Then…. they arrive to nodes in a stochastic fashion…and then…each router asynchronously elaborates them…
Of course notice that.. if the traffic intensity exceed some given quantities …well some traffic is lost due to buffer overflows…
Let us further note that queuing networks are successfully used not only to solve resource allocation problems in telecommunication but…. Of course….whenever a flow of jobs need to be processed, independently by the fact that their arrivals and services are either synchronous or asynchronous, or either stochastic or deterministic.
In particular we have that all the results we are going to see are useful to determines in an easy way the system performance…and also to evaluate…. for resource allocation purposes…. the resources need such that a complex client-server architecture works while satisfying some QoS specifications.
Specification that could be expressed in term of time spent in the system…or in term of the buffer capacity … and that of course depends on the allocated resources…that means the number of servers per queue, their service rate… the buffer capacity … furthermore it is easy understand that all those quantities are further influenced by the costumer routing that express…in terms or probability….all the possible paths that a costumer can follows within the network.

## Slide 13: The Augmented Lagrangian and Control Interpretation
Let us now note that the solution of (15), reported also below
is also equivalent to the solution of the next augment Lagrangian problem
Indeed, it is easy note that, if the constraint is satisfied
Note: It is interesting note solver (18) has a proportional-integral (PI) term w.r.t. the consenus error
Thus, by straightforward considerations, the next solver is derived:
Note: The extra dampling term provides better stability and convergence properties, and allows relaxing the assumption is strictly convex to just convex
Notes: Here just to remark the importance of queuing networks in telecommunication systems we have another example…for instance…the Internet… that….as you know…. It works by means of a complex architecture where packets flows are processed by many routers, each modeled by a queue.
In particular we have that packets enter in the network because generated from different sources…. and with different destinations…
Then…. they arrive to nodes in a stochastic fashion…and then…each router asynchronously elaborates them…
Of course notice that.. if the traffic intensity exceed some given quantities …well some traffic is lost due to buffer overflows…
Let us further note that queuing networks are successfully used not only to solve resource allocation problems in telecommunication but…. Of course….whenever a flow of jobs need to be processed, independently by the fact that their arrivals and services are either synchronous or asynchronous, or either stochastic or deterministic.
In particular we have that all the results we are going to see are useful to determines in an easy way the system performance…and also to evaluate…. for resource allocation purposes…. the resources need such that a complex client-server architecture works while satisfying some QoS specifications.
Specification that could be expressed in term of time spent in the system…or in term of the buffer capacity … and that of course depends on the allocated resources…that means the number of servers per queue, their service rate… the buffer capacity … furthermore it is easy understand that all those quantities are further influenced by the costumer routing that express…in terms or probability….all the possible paths that a costumer can follows within the network.

## Slide 14: CT distributed Convex optimization: Simulink Simulation
Note: Least square opt. converges to
Notes: Here just to remark the importance of queuing networks in telecommunication systems we have another example…for instance…the Internet… that….as you know…. It works by means of a complex architecture where packets flows are processed by many routers, each modeled by a queue.
In particular we have that packets enter in the network because generated from different sources…. and with different destinations…
Then…. they arrive to nodes in a stochastic fashion…and then…each router asynchronously elaborates them…
Of course notice that.. if the traffic intensity exceed some given quantities …well some traffic is lost due to buffer overflows…
Let us further note that queuing networks are successfully used not only to solve resource allocation problems in telecommunication but…. Of course….whenever a flow of jobs need to be processed, independently by the fact that their arrivals and services are either synchronous or asynchronous, or either stochastic or deterministic.
In particular we have that all the results we are going to see are useful to determines in an easy way the system performance…and also to evaluate…. for resource allocation purposes…. the resources need such that a complex client-server architecture works while satisfying some QoS specifications.
Specification that could be expressed in term of time spent in the system…or in term of the buffer capacity … and that of course depends on the allocated resources…that means the number of servers per queue, their service rate… the buffer capacity … furthermore it is easy understand that all those quantities are further influenced by the costumer routing that express…in terms or probability….all the possible paths that a costumer can follows within the network.

## Slide 15: Distributed DT convex optimization
For simplicity in the analysis, we considered solvers performing the minimization in CT
However, results can easily be extended in the DT setting by means of Euler-discretization, e.g.:
Then, by looking for a Lyapunov function such that ), upper-bounds for , which will depends also by could be found.
Example: Let be quadratic, , then following a simpler eigenvalue analisys it results (i.e. condition for contraction) holds for all .
Notes: Here just to remark the importance of queuing networks in telecommunication systems we have another example…for instance…the Internet… that….as you know…. It works by means of a complex architecture where packets flows are processed by many routers, each modeled by a queue.
In particular we have that packets enter in the network because generated from different sources…. and with different destinations…
Then…. they arrive to nodes in a stochastic fashion…and then…each router asynchronously elaborates them…
Of course notice that.. if the traffic intensity exceed some given quantities …well some traffic is lost due to buffer overflows…
Let us further note that queuing networks are successfully used not only to solve resource allocation problems in telecommunication but…. Of course….whenever a flow of jobs need to be processed, independently by the fact that their arrivals and services are either synchronous or asynchronous, or either stochastic or deterministic.
In particular we have that all the results we are going to see are useful to determines in an easy way the system performance…and also to evaluate…. for resource allocation purposes…. the resources need such that a complex client-server architecture works while satisfying some QoS specifications.
Specification that could be expressed in term of time spent in the system…or in term of the buffer capacity … and that of course depends on the allocated resources…that means the number of servers per queue, their service rate… the buffer capacity … furthermore it is easy understand that all those quantities are further influenced by the costumer routing that express…in terms or probability….all the possible paths that a costumer can follows within the network.

## Slide 16: Asynchronous Gossip-based Optimization
To account gossip-based asynchronous communications the DT consensus algorithm
has been rewritten as
where
node denotes a neighbor of taken random with probability
node denotes the node is randomly waked-up at with probability
Similarly, the DT optimization solver on the right can be rewritten in gossip fashion as
Note: If this lead (zig-zag motion around ), thus consider a vanishing step-size may improve the solver accuracy since .
For instance let be the #times agent updated its state because of either or , then consider is vanishing and it improves the accuracy since
Proof idea: First we need to show reachs a consensus (see gossip consensus proof). Then, that by descending the gradient direction. See: [Nedic & Veeravalli (2009). IEEE CDC]
Due to (*.1), one note that achieves the consensus on the implies also makes consensus.
Thus, a simpler and elegant version of (*) is:
Notes: Here just to remark the importance of queuing networks in telecommunication systems we have another example…for instance…the Internet… that….as you know…. It works by means of a complex architecture where packets flows are processed by many routers, each modeled by a queue.
In particular we have that packets enter in the network because generated from different sources…. and with different destinations…
Then…. they arrive to nodes in a stochastic fashion…and then…each router asynchronously elaborates them…
Of course notice that.. if the traffic intensity exceed some given quantities …well some traffic is lost due to buffer overflows…
Let us further note that queuing networks are successfully used not only to solve resource allocation problems in telecommunication but…. Of course….whenever a flow of jobs need to be processed, independently by the fact that their arrivals and services are either synchronous or asynchronous, or either stochastic or deterministic.
In particular we have that all the results we are going to see are useful to determines in an easy way the system performance…and also to evaluate…. for resource allocation purposes…. the resources need such that a complex client-server architecture works while satisfying some QoS specifications.
Specification that could be expressed in term of time spent in the system…or in term of the buffer capacity … and that of course depends on the allocated resources…that means the number of servers per queue, their service rate… the buffer capacity … furthermore it is easy understand that all those quantities are further influenced by the costumer routing that express…in terms or probability….all the possible paths that a costumer can follows within the network.

## Slide 17: Asynchronous Gossip-based Convex Optimization
clc, clear all, close all, rng(0)
% Problem: min_x sum_i (x_i(t)-x_i(0))^2 s.t. Lx=0 in a gossip fashion
% The graph G is complete for simplicity in the simulation’s implementation.
% However, if G is arbitrary, it is must be undirected and connected
N=10 % Number of agents
% Set the number of iterations
num_iters = 2000;
% Support vector to store data at each iteration
x_sol=zeros(num_iters,N);
v_sol=zeros(num_iters,N);
counter=zeros(num_iters,N);
t = 0; % Interaction time
% Initialize the agents states, i.e., set x(0)
x0=[1 2 3 4 5 6 7 8 9 50]
x_sol(1,:)=x0;
Notes: Here just to remark the importance of queuing networks in telecommunication systems we have another example…for instance…the Internet… that….as you know…. It works by means of a complex architecture where packets flows are processed by many routers, each modeled by a queue.
In particular we have that packets enter in the network because generated from different sources…. and with different destinations…
Then…. they arrive to nodes in a stochastic fashion…and then…each router asynchronously elaborates them…
Of course notice that.. if the traffic intensity exceed some given quantities …well some traffic is lost due to buffer overflows…
Let us further note that queuing networks are successfully used not only to solve resource allocation problems in telecommunication but…. Of course….whenever a flow of jobs need to be processed, independently by the fact that their arrivals and services are either synchronous or asynchronous, or either stochastic or deterministic.
In particular we have that all the results we are going to see are useful to determines in an easy way the system performance…and also to evaluate…. for resource allocation purposes…. the resources need such that a complex client-server architecture works while satisfying some QoS specifications.
Specification that could be expressed in term of time spent in the system…or in term of the buffer capacity … and that of course depends on the allocated resources…that means the number of servers per queue, their service rate… the buffer capacity … furthermore it is easy understand that all those quantities are further influenced by the costumer routing that express…in terms or probability….all the possible paths that a costumer can follows within the network.

## Slide 18: Asynchronous Gossip-based Convex Optimization
for i = 2:num_iters
  % Randomly select two nodes to communicate
  node_indices = randperm(N, 2);
  node1 = node_indices(1);
  node2 = node_indices(2);
  % Update the counter counting how many times each node is called
  counter(i,node1)=counter(i-1,node1)+1;
  counter(i,node2)=counter(i-1,node2)+1;
  % Update the Langrange multiplier in a gossip fashion
  v_sol(i,node1) = (x_sol(i-1,node1) + x_sol(i-1, node2)) / 2;
  v_sol(i,node2) = (x_sol(i-1,node1) + x_sol(i-1, node2)) / 2;
  % Update the decision variables along the gradient-descent direction using a vanishing step-size
  x_sol(i,node1) = v_sol(i,node1) - 2*(x_sol(i-1,node1) - x0(node1))/counter(i,node1);
  x_sol(i,node2) = v_sol(i,node2) - 2*(x_sol(i-1,node1) - x0(node2))/counter(i,node2);
  for k=1:N
    if k~=node1 && k ~= node2
      v_sol(i,k)=v_sol(i-1,k);
      x_sol(i,k)=x_sol(i-1,k);
      counter(i,k)=counter(i-1,k);
  end
  end
  t = [t;t(end) + exprnd(1/N)]; % Update the interaction time as Exp. Inter-event random time
end
Notes: Here just to remark the importance of queuing networks in telecommunication systems we have another example…for instance…the Internet… that….as you know…. It works by means of a complex architecture where packets flows are processed by many routers, each modeled by a queue.
In particular we have that packets enter in the network because generated from different sources…. and with different destinations…
Then…. they arrive to nodes in a stochastic fashion…and then…each router asynchronously elaborates them…
Of course notice that.. if the traffic intensity exceed some given quantities …well some traffic is lost due to buffer overflows…
Let us further note that queuing networks are successfully used not only to solve resource allocation problems in telecommunication but…. Of course….whenever a flow of jobs need to be processed, independently by the fact that their arrivals and services are either synchronous or asynchronous, or either stochastic or deterministic.
In particular we have that all the results we are going to see are useful to determines in an easy way the system performance…and also to evaluate…. for resource allocation purposes…. the resources need such that a complex client-server architecture works while satisfying some QoS specifications.
Specification that could be expressed in term of time spent in the system…or in term of the buffer capacity … and that of course depends on the allocated resources…that means the number of servers per queue, their service rate… the buffer capacity … furthermore it is easy understand that all those quantities are further influenced by the costumer routing that express…in terms or probability….all the possible paths that a costumer can follows within the network.

## Slide 19: Gossip-based implementation
% Print the final node values
figure(1)
subplot(121)
  stairs(t,x_sol)
  title('Agents convergence $x^*=9.5\cdot 1_n$')
  xlabel('$t$')
  ylabel('$x_i(t)$')
  axis([0 150 -50 50])
  yticks([-50:10:50])
  grid
subplot(122)
  stairs(t,x_sol)
  title('Zoom')
  xlabel('$t$')
  axis([150 200 9 11])
  grid
Notes: Here just to remark the importance of queuing networks in telecommunication systems we have another example…for instance…the Internet… that….as you know…. It works by means of a complex architecture where packets flows are processed by many routers, each modeled by a queue.
In particular we have that packets enter in the network because generated from different sources…. and with different destinations…
Then…. they arrive to nodes in a stochastic fashion…and then…each router asynchronously elaborates them…
Of course notice that.. if the traffic intensity exceed some given quantities …well some traffic is lost due to buffer overflows…
Let us further note that queuing networks are successfully used not only to solve resource allocation problems in telecommunication but…. Of course….whenever a flow of jobs need to be processed, independently by the fact that their arrivals and services are either synchronous or asynchronous, or either stochastic or deterministic.
In particular we have that all the results we are going to see are useful to determines in an easy way the system performance…and also to evaluate…. for resource allocation purposes…. the resources need such that a complex client-server architecture works while satisfying some QoS specifications.
Specification that could be expressed in term of time spent in the system…or in term of the buffer capacity … and that of course depends on the allocated resources…that means the number of servers per queue, their service rate… the buffer capacity … furthermore it is easy understand that all those quantities are further influenced by the costumer routing that express…in terms or probability….all the possible paths that a costumer can follows within the network.

## Slide 20: Asynchronous Gossip-based Convex Optimization
Notes: Here just to remark the importance of queuing networks in telecommunication systems we have another example…for instance…the Internet… that….as you know…. It works by means of a complex architecture where packets flows are processed by many routers, each modeled by a queue.
In particular we have that packets enter in the network because generated from different sources…. and with different destinations…
Then…. they arrive to nodes in a stochastic fashion…and then…each router asynchronously elaborates them…
Of course notice that.. if the traffic intensity exceed some given quantities …well some traffic is lost due to buffer overflows…
Let us further note that queuing networks are successfully used not only to solve resource allocation problems in telecommunication but…. Of course….whenever a flow of jobs need to be processed, independently by the fact that their arrivals and services are either synchronous or asynchronous, or either stochastic or deterministic.
In particular we have that all the results we are going to see are useful to determines in an easy way the system performance…and also to evaluate…. for resource allocation purposes…. the resources need such that a complex client-server architecture works while satisfying some QoS specifications.
Specification that could be expressed in term of time spent in the system…or in term of the buffer capacity … and that of course depends on the allocated resources…that means the number of servers per queue, their service rate… the buffer capacity … furthermore it is easy understand that all those quantities are further influenced by the costumer routing that express…in terms or probability….all the possible paths that a costumer can follows within the network.

## Slide 21: References
Wang & Elia (2011). A control perspective for centralized and distributed convex optimization. IEEE Conf. Decision and Control.
Polyak (1987). Introduction to optimization. optimization software." Inc., Pub. Div., NY (USA)
Nedic & Veeravalli (2009). Asynchronous gossip algorithms for stochastic optimization. IEEE Conf. on Decision and Control, pp. 3581-3586.
Franceschelli, Pilloni, Gasparri (2020). Multi-agent coordination of thermostatically controlled loads by smart power sockets for electric demand-side management. IEEE Transaction on Control Systems Technology, 29.2 (2020): 731-743.
Pilloni, Pisano, Franceschelli, Usai (2023) “On the variable structure control approach with sliding modes to robust finite-time consensus problems: A methodological overview based on nonsmooth analysis”. In: Annual Reviews in Control.
Pilloni, Pisano, Franceschelli, Usai (2016). A discontinuous algorithm for distributed convex optimization. In: Int. Workshop on Variable Structure Systems, pp. 22-27.
Related results & research activities developed at the “AutoLab” Research Group
Robust consensus and optimizations problems using nonlinear discontinuous algorithms
Energy Communities Demand-side management optimization problems over IoT infrastructures
Kaheni, Pilloni, Ruda, Usai, Franceschelli (2022). Distributed Asynchronous Greedy Control of Large Networks of Thermostatically Controlled Loads for Electric Demand Response. IEEE Control Systems Letters, 7, pp. 169-174.
Pilloni, Callia, Pisano, Usai (2024) “Strict Lyapunov Functions for Second-Order Sliding Mode Robust Consensus with the Super-Twisting Algorithm”. In: 17th Int. Workshop on Variable Structure Systems (under review).
Moré, Deplano, Pilloni, Pisano, Franceschelli (2024). Online Coordination of BESS and Thermostatically Control Loads for Shared Energy Optimization in Energy Communities. IEEE Int. Conf. on Automation Science and Engineering (CASE), pp. 2738-2744.
Gharesifard, Bahman, and Jorge Cortés. "Distributed continuous-time convex optimization on weight-balanced digraphs." IEEE Transactions on Automatic Control 59.3 (2013): 781-786.
Notes: Here just to remark the importance of queuing networks in telecommunication systems we have another example…for instance…the Internet… that….as you know…. It works by means of a complex architecture where packets flows are processed by many routers, each modeled by a queue.
In particular we have that packets enter in the network because generated from different sources…. and with different destinations…
Then…. they arrive to nodes in a stochastic fashion…and then…each router asynchronously elaborates them…
Of course notice that.. if the traffic intensity exceed some given quantities …well some traffic is lost due to buffer overflows…
Let us further note that queuing networks are successfully used not only to solve resource allocation problems in telecommunication but…. Of course….whenever a flow of jobs need to be processed, independently by the fact that their arrivals and services are either synchronous or asynchronous, or either stochastic or deterministic.
In particular we have that all the results we are going to see are useful to determines in an easy way the system performance…and also to evaluate…. for resource allocation purposes…. the resources need such that a complex client-server architecture works while satisfying some QoS specifications.
Specification that could be expressed in term of time spent in the system…or in term of the buffer capacity … and that of course depends on the allocated resources…that means the number of servers per queue, their service rate… the buffer capacity … furthermore it is easy understand that all those quantities are further influenced by the costumer routing that express…in terms or probability….all the possible paths that a costumer can follows within the network.